## Slide 1: Principles of Neuroimaging
Friday, February 25th@ 8 a.m., MSB 2.006
M1 Medical Neuroscience. Nachum Dafny, Course Director
Assistant Professor
Department of Neurobiology and Anatomy
Michael.S.Beauchamp@uth.tmc.edu
Michael S. Beauchamp, Ph.D.

## Slide 2: Why is neuroimaging difficult?
2 - 17
17 - 21
21 - 23
Notes: CNS is soft tissue surrounded by hard bone

## Slide 3: Palpation/Sensation
skull: can’t feel much from outside (sorry, ultrasound)
-no nerves in brain: can’t feel much from inside

## Slide 4: Alphabet Soup
CT
MRI
SPECT
PET
MEG
EEG
fMRI

## Slide 5: Taxonomy of Neuroimaging Methods
Neuroimaging Methods
External Ionizing Radiation
Internal Ionizing Radiation
Non-ionizing radiation
(Radio Waves)
CT
PET
SPECT
MRI
fMRI
Diffusion Imaging (DWI/DTI)
MR Angiography
MR Spectroscopy
Angiogram/
Arteriogram
X-Ray
(radiograph)
Accessory (non-imaging)
Methods
MEG
EEG

## Slide 6: Taxonomy of Neuroimaging Methods
Neuroimaging Methods
External Ionizing Radiation
Internal Ionizing Radiation
Non-ionizing radiation
(Radio Waves)
CT
PET
SPECT
MRI
fMRI
Diffusion Imaging (DWI/DTI)
MR Angiography
MR Spectroscopy
Angiogram/
Arteriogram
X-Ray
(radiograph)
Accessory (non-imaging)
Methods
MEG
EEG

## Slide 7: Taxonomy of Neuroimaging Methods
Neuroimaging Methods
External Ionizing Radiation
Internal Ionizing Radiation
Non-ionizing radiation
(Radio Waves)
CT
PET
SPECT
MRI
fMRI
Diffusion Imaging (DWI/DTI)
MR Angiography
MR Spectroscopy
Angiogram/
Arteriogram
X-Ray
(radiograph)
Accessory (non-imaging)
Methods
MEG
EEG

## Slide 8: X-Ray (radiograph)—bones, not brain! (tissue density)

## Slide 9: Taxonomy of Neuroimaging Methods
Neuroimaging Methods
External Ionizing Radiation
Internal Ionizing Radiation
Non-ionizing radiation
(Radio Waves)
CT
PET
SPECT
MRI
fMRI
Diffusion Imaging (DWI/DTI)
MR Angiography
MR Spectroscopy
Angiogram/
Arteriogram
X-Ray
(radiograph)
Accessory (non-imaging)
Methods
MEG
EEG

## Slide 10: Arteriogram (a.k.a. Angiogram)
Basic principle: Inject contrast agent (dye)
that is radio-opaque i.e. iodine containing agents
Notes: Dangerous because have to feed a catheter up through the vessels—if puncture one then big trouble

## Slide 11: Taxonomy of Neuroimaging Methods
Neuroimaging Methods
External Ionizing Radiation
Internal Ionizing Radiation
Non-ionizing radiation
(Radio Waves)
CT
PET
SPECT
MRI
fMRI
Diffusion Imaging (DWI/DTI)
MR Angiography
MR Spectroscopy
Angiogram/
Arteriogram
X-Ray
(radiograph)
Accessory (non-imaging)
Methods
MEG
EEG

## Slide 12: CT (computed tomography)

## Slide 13: CT (computed tomography)
Pros:
Widely available
Very fast to collect whole-head images
(one slice in < 1 ms; whole head in ~ seconds; whole exam in 10 minutes )
Somewhat cheaper than MRI
(~$500 vs ~$1000 for MRI)
Less hassle (few contraindications)
Best for an emergency
Cons:
Exposure to ionizing radiation (increased risk of cancer)
can require a contrast agent—for brain, injectable iodine compound
Poor tissue contrast
not versatile

## Slide 14: CT (computed tomography)
Basic Principle: rotate machinery
to take multiple x-rays with different paths through the body

## Slide 15: Common clinical use: stroke
Patient presents with stroke
80%
Give tPA, dissolve clot,
Blood flow restored,
Patient recovers
Give tPA, prevent clotting,
Patient dies of massive bleed
20%
ischemic
hemorraghic

## Slide 16: Common clinical use: stroke
Patient presents with stroke
80%
20%
ischemic
hemorraghic

## Slide 17: CT (computed tomography)
Pros:
Widely available
Very fast to collect whole-head images
(one slice in < 1 ms; whole head in ~ seconds; whole exam in 10 minutes )
Somewhat cheaper than MRI
(~$500 vs ~$1000 for MRI)
Less hassle (few contraindications)
Best for an emergency
Cons:
Exposure to ionizing radiation (increased risk of cancer)
can require a contrast agent—for brain, injectable iodine compound
Poor tissue contrast
not versatile

## Slide 18
Neuroimaging Methods
External Ionizing Radiation
Internal Ionizing Radiation
Non-ionizing radiation
(Radio Waves)
CT
PET
SPECT
MRI
fMRI
Diffusion Imaging (DWI/DTI)
MR Angiography
MR Spectroscopy
Angiogram/
Arteriogram
X-Ray
(radiograph)
Accessory (non-imaging)
Methods
MEG
EEG

## Slide 19: “Nuclear Medicine”
Neuroimaging Methods
External Ionizing Radiation
Internal Ionizing Radiation
Non-ionizing radiation
(Radio Waves)
CT
PET
SPECT
MRI
fMRI
Diffusion Imaging (DWI/DTI)
MR Angiography
MR Spectroscopy
Angiogram/
Arteriogram
X-Ray
(radiograph)
Accessory (non-imaging)
Methods
MEG
EEG

## Slide 20: “Nuclear Medicine”: PET/SPECT
Basic priniciple:
Inject radioactive isotope attached to metabolic compound (Oxygen, Glucose, etc.)
Wait for it to decay, look for radioactive decay products

## Slide 21: PET/SPECT
Pros:
Fairly cheap (~ $1000)
Shows function (metabolism)
Cons:
Exposure to ionizing radiation (increased risk of cancer)
~1 year of background radiation
Low-resolution
Slow to very slow
not versatile

## Slide 22: SPECT Single Photon Emission Computed Tomography
“Nuclear Medicine”: ~unclear medicine

## Slide 23: SPECT Single Photon Emission Computed Tomography
Radionuclides
  Single-Gamma emitting
  99mTc, 123I, 67Ga, 111In

## Slide 24: PET: Positron Emission Tomography
Basic priniciple:
Inject radioactive isotope attached to important metabolic compound (Oxygen, Glucose)
Wait for it to decay.
Pick up two particles going in opposite directions—improves spatial resolution
PET uses beta-plus-emitting radionuclides such as C-11, N-13, O-15, and F-18 which annihilate into two 511-keV photons that travel in opposite directions.

## Slide 25: Developments in PET
Development of new radiotracers
Joshi et al., JCBFM 2009
[11C]DTBZ
VMAT2
~dopamine,serotonin
[11C] Flumazenil
(benzodiazepine receptor antagonist
~ GABA-A )
[11C]PMP
Substrate for AChE

## Slide 26: 2 –photons instead of one  better resolution

## Slide 27: Sample Clinical Application: Alzheimer’s Diagnosis
Compounds that bind to AD plaques
Conditional approval by FDA (Jan 2011)
C. M. Clark et al. J. Am. Med. Assoc. 305, 275–283; 2011

## Slide 28
Neuroimaging Methods
External Ionizing Radiation
Internal Ionizing Radiation
Non-ionizing radiation
(Radio Waves)
CT
PET
SPECT
MRI
fMRI
Diffusion Imaging (DWI/DTI)
MR Angiography
MR Spectroscopy
Angiogram/
Arteriogram
X-Ray
(radiograph)
Accessory (non-imaging)
Methods
MEG
EEG

## Slide 29: MRI: Magnetic Resonance Imaging
Pros:
incredible images
advancing very rapidly
extremely high resolution
extremely versatile
NO ionizing radiation
Cons:
moderately expensive (~$1000)
complex
some contraindications
Can require injection of contrast agents (Gadolinium/Iron compounds)

## Slide 30: Imaging Techniques: MRI
the MR scanner is a giant magnet: 1.5T, 3T, 7T, 9T

## Slide 31
Notes: Left—CT; right—MRI

## Slide 32: Contraindications I
Ferrous metal in body

## Slide 33: Contraindications II
Cochlear implants (always)
Maybe: pacemakers, vagal nerve stimulators, old (> 20 year) surgical implants

## Slide 34: Clinical Applications

## Slide 35: UTH MRI Facility
Location: Ground Floor, MSB Building
Equipment: Phillips 3T whole body human MRI scanner
Bruker 7T small animal (rodent) scanner
Mock scanner for testing and training

## Slide 36: MRI (Magnetic Resonance Imaging)
Basic principle: uses radio waves to interrogate protons in water molecules in the brain

## Slide 37: MRI (Magnetic Resonance Imaging)
Basic principle: uses radio waves to interrogate protons in water molecules in the brain

## Slide 38
128 MHz at 3T (~ FM Radio)

## Slide 39: We listen to these radio waves with an “RF coil” (radio antenna)
H2O
H2O
H2O

## Slide 40: B0 = Giant Field Produced by Giant Magnet
Purpose is to align H protons in H2O (little magnets)
[Little magnets lining up with external lines of force]
[Main magnet and some of its lines of force]

## Slide 41
Small B0 produces
small net
magnetization M
Thermal motions
try to randomize
alignment of
proton magnets
Larger B0 produces
larger net
magnetization M,
lined up with B0
Reality check:
0.0003% of protons
aligned per Tesla
of B0

## Slide 42: Precession of Magnetization M
If M is not parallel to B, then
it precesses clockwise around
the direction of B.
However, “normal” (fully relaxed) situation has M parallel to B, which means there won’t be any
precession
Magnetic field causes M to rotate (or precess) about the direction of B at a frequency proportional to the size of B — 42 million times per second (42 MHz), per Tesla of B
N.B.: part of M parallel to B (Mz)
does not precess

## Slide 43: B1 = Excitation (Transmitted) Radio Frequency (RF) Field
The effect of the tiny B1 is
to cause M to spiral away
from the direction of the
static B field
B110–4 Tesla
This is called resonance
If B1 frequency is not close to
resonance, B1 has no effect
Left alone, M will align itself with B in about 2–3 s
So don’t leave it alone: apply (transmit) a magnetic field B1 that fluctuates at the precession frequency and points perpendicular to B0
Time = 2–4 ms

## Slide 44: Relaxation: Nothing Lasts Forever
In absence of external B1, M will go back to being aligned with static field B0 — this is called relaxation
T2: Part of M perpendicular to B0 shrinks [Mxy]
  This part of M is called transverse magnetization
  It provides the detectable RF signal
T1: Part of M parallel to B0 grows back [Mz]
  This part of M is called longitudinal magnetization
  Not directly detectable, but is converted into transverse magnetization by externally applied B1

## Slide 45: Ants on a Pole analogy—two different physical properties

## Slide 46
Bitar, R. et al. Radiographics 2006;26:513-537

## Slide 48: Basics of MR
T1 ~ Longitudinal Magnetization/Relaxation
“hi-resolution, normal anatomy”
T2 ~ Transverse Magnetization/Relaxation
“pathology”—water content
Notes: Show MRIcron

## Slide 49: Basics of MR—contrast agents
Gadolinium
can be injected to enhance contrast (usually in T1 images); hastens T1 recovery making image brighter

## Slide 50: Clinical Applications: Multiple Sclerosis
T2 is best for seeing white matter abnormalities

## Slide 51: Bonus—Shelf Exam Question
A 53-year-old woman dies 4 days after an automobile
collision. She sustained multiple injuries including a
femoral fracture. Widespread petechiae are found in the
cerebral white matter at autopsy. Which of the following is
the most likely cause of these findings?
(A) Acute respiratory distress syndrome
(B) Contrecoup injury
(C) Fat embolization
(D) Septicemia
(E) Subdural hematoma

## Slide 52: Fat emboli (FLAIR T2)

## Slide 53: Scanner as computer…
pulse sequences are software
CT vs MRI
TV with one channel (not that much good on)
vs.
Computer that can run lots of programs (takes longer to boot up, but get more for it)

## Slide 54
Neuroimaging Methods
External Ionizing Radiation
Internal Ionizing Radiation
Non-ionizing radiation
(Radio Waves)
CT
PET
SPECT
MRI
fMRI
Diffusion Imaging (DWI/DTI)
MR Angiography
MR Spectroscopy
Angiogram/
Arteriogram
X-Ray
(radiograph)
Accessory (non-imaging)
Methods
MEG
EEG

## Slide 55: MRI vs. fMRI
MRI studies brain anatomy.
Functional MRI (fMRI) studies brain function.
fMRI for Dummies

## Slide 56: An “anonymous” M3

## Slide 57: An “anonymous” M3

## Slide 58
MRI vs. fMRI
 neural activity   blood oxygen   fMRI signal
MRI
fMRI
one image
many images
(e.g., every 2 sec for 5 mins)
high resolution
(1 mm)
low resolution
(~3 mm but can be better)
fMRI
Blood Oxygenation Level Dependent (BOLD) signal
  indirect measure of neural activity
…
fMRI for Dummies

## Slide 59: An “anonymous” M3

## Slide 60: Metabolism
Brain uses ~20% of total body oxygen
(even though only 1-2% of total body mass)
Complex mechanism for regulating cerebral blood flow to ensure adequate oxygen supply

## Slide 61: Deoxygenated blood attenuates T2*-weighted MR images
MRI volume element
O2
Notes: to emphasize that only the venous circulation matters in fMRI, I drew this schematic figure showing how deoxyhemoglobin arises in tissues. This square region [point] represents a perfused tissue volume element. These light blue molecules represent water within the tissue, which produces most of the MRI signal. The flow of blood through the volume element is regulated by varying the tone of smooth muscles in the walls of small arterial vessels. Arterial dHb levels are negligible in healthy individuals, though, so the arterial blood doesn’t normally influence the BOLD signal. In the capillaries, oxygen is removed from HbO2, introducing blue, paramagnetic deoxyhemoglobin into the venous circulation.
this scenario occurs in every volume element of an MR image; for our purposes, arterial blood can be ignored and we need only consider the state of venous blood throughout the brain, which is uniformly blue at rest.
During increased perfusion, venous blood almost always becomes redder, though.

## Slide 62: decrease of venous dHb during increased perfusion:
O2
Notes: This slide illustrates the two MRI-relevant consequences of increased cerebral blood flow.
Increased oxygenation of venous blood, shown by coloring the blood violet here, is by far the most important effect, as it causes the tissue MR signal to decay more slowly and makes decay-sensitive images brighter.
A secondary consequence of increased perfusion is a passive inflation of the highly compliant venous vessels, whose walls lack the muscular tone of the arteriolar vessels used to regulate perfusion. This causes an increase in Cerebral Blood Volume.
The increase in venous blood volume adds to the total amount of dHb in the tissue volume element, slightly counteracting the dilution of dHb caused by the increase in blood supply.
Although these two effects - blood volume and deoxyhemoglobin dilution - compete, the dilution effect is by far the dominant one.

## Slide 63: Human 3T used for BOLD fMRI

## Slide 64
Graphs vs. time of 33 voxel region
One Fast Image
Overlay on Anatomy
68 points in time 5 s apart; 16 slices of 6464 images
This voxel did
not respond
Colored voxels responded to the mental
stimulus alternation, whose pattern is shown in the
yellow reference curve plotted in the central voxel

## Slide 65
Notes: fMRI used for presurgical mapping—find brains areas important for motor/language so surgeon doesn’t damage them

## Slide 67
Neuroimaging Methods
External Ionizing Radiation
Internal Ionizing Radiation
Non-ionizing radiation
(Radio Waves)
CT
PET
SPECT
MRI
fMRI
Diffusion Imaging (DWI/DTI)
MR Angiography
MR Spectroscopy
Angiogram/
Arteriogram
X-Ray
(radiograph)
Accessory (non-imaging)
Methods
MEG
EEG

## Slide 68: Diffusion Weighted Imaging—earliest post-stroke diagnosis

## Slide 69: MR Angiography
Notes: Show movie

## Slide 70: Magnetic Resonance Spectroscopy
reduced GABA in panic disorder

## Slide 71: Cortical Surface Models—AD/PD
Notes: The thickness of gray matter is a sensitive measure of pathology, and can provide early diagnosis of Alzheimer’s and Parkinson’s

## Slide 72
Neuroimaging Methods
External Ionizing Radiation
Internal Ionizing Radiation
Non-ionizing radiation
(Radio Waves)
CT
PET
SPECT
MRI
fMRI
Diffusion Imaging (DWI/DTI)
MR Angiography
MR Spectroscopy
Angiogram/
Arteriogram
X-Ray
(radiograph)
Accessory (non-imaging)
Methods
MEG
EEG

## Slide 74: EEG/MEG
Pros:
Completely non-invasive—only modality that NEVER requires injection of a contrast agent
no ionizing radiation
direct measurement of neuronal activity
Cons:
not really neuroimaging
Limited clinical utility:
EEG—sleep studies
MEG--epilepsy

## Slide 76: EEG
basic priniciple: electrodes on scalp surface record summed electrical activity (mainly synaptic)
of many neurons

## Slide 77: MEG Scanner
basic priniciple: sensors near scalp surface record summed magnetic field resulting from
electrical activity (mainly synaptic) of many neurons

## Slide 78: EEG/MEG Results
EEG Activation Map
MEG Activation Map
Notes: Sometimes EEG/MEG are combined with MRI for greater resolution.

## Slide 79: Taxonomy of Neuroimaging Methods
Neuroimaging Methods
External Ionizing Radiation
Internal Ionizing Radiation
Non-ionizing radiation
(Radio Waves)
CT
PET
SPECT
MRI
fMRI
Diffusion Imaging (DWI/DTI)
MR Angiography
MR Spectroscopy
Angiogram/
Arteriogram
X-Ray
(radiograph)
Accessory (non-imaging)
Methods
MEG
EEG

## Slide 80: Want to know more?
MS4 Elective: BSCI Advances in Translational Neuroimaging (Independent Study)
This elective will expose students to advances in translational neuroimaging. No technical background or experience with neuroimaging is required. Students will present the results of their literature review in a small group format. Meetings will be held once a week, with flexible scheduling to accommodate residency interviews; the majority of the effort will be in self-directed study.